## Slide 1
LOCK
DDCA MINI PROJECT
Design and Simulation of a Smart Home Security System
Digital Design and Computer Architecture
Team Members: Vayyala Dhikshitha – 2620030310
Neerukonda Charishma Chowdari – 2620030311
Yuthikaa Bellamkonda -
Section: Section - 2
Faculty: Dayarnab
COMBINATIONAL LOGIC • LOGISIM

## Slide 2
Problem Statement & Objective
2/7
PROBLEM STATEMENT
A home security system should detect possible intrusion and activate an alarm only when the system is armed.
OBJECTIVES
Detect door opening
Detect window opening
Detect motion
Activate alarm only when security is armed
Implement using basic logic gates
Simulate and verify in Logisim
CONCEPTUAL BLOCK DIAGRAM
Door Sensor
Window Sensor
Motion Sensor
Security System
LOGIC SYSTEM
ALARM
Sensor signals → Boolean logic → Alarm output

## Slide 3
System Inputs, Output and Boolean Expression
3/7
Signal
Meaning
0
1
S
Security system
Disarmed
Armed
D
Door sensor
Closed
Open
W
Window sensor
Closed
Open
M
Motion sensor
No motion
Motion detected
A
Alarm output
OFF
ON
BOOLEAN EXPRESSION
A = S(D + W + M)
HOW IT WORKS
OR: any intrusion sensor is active
AND: alarm activates only when armed
A = S AND (D OR W OR M) Alarm is ON only if S = 1 and at least one sensor is active.

## Slide 4
Combinational Logic Circuit
4/7
LOGIC STRUCTURE
D — Door
W — Window
M — Motion
OR
3-input OR
AND
Alarm A
S — Security
CIRCUIT COMPONENTS
One 3-input OR gate and one 2-input AND gate
Four input switches (S, D, W, M) and one output LED

## Slide 5
Truth Table & Logic Verification
5/7
S
D
W
M
A
0
0
0
0
0
0
0
0
1
0
0
0
1
0
0
0
0
1
1
0
0
1
0
0
0
0
1
0
1
0
0
1
1
0
0
0
1
1
1
0
1
0
0
0
0
1
0
0
1
1
1
0
1
0
1
1
0
1
1
1
1
1
0
0
1
1
1
0
1
1
1
1
1
0
1
1
1
1
1
1
Boolean expression
A = S(D + W + M)
When S = 0, the alarm is always OFF. When S = 1, any active sensor turns it ON.
Highlighted rows: Alarm = 1

## Slide 6
Logisim Simulation and Test Cases
6/7
Test the input switches and confirm that the LED matches the expected alarm state.
Case
S
D
W
M
Expected A
1
0
1
0
0
0
2
1
1
0
0
1
3
1
0
1
0
1
4
1
0
0
1
1
5
1
0
0
0
0
＋ INSERT LOGISIM SIMULATION SCREENSHOT HERE
＋ INSERT SECOND SCREENSHOT SHOWING ALARM ON
SIMULATION CHECKLIST
Case 1: disarmed → alarm OFF
Cases 2–4: armed + intrusion → alarm ON
Case 5: armed + no intrusion → alarm OFF

## Slide 7
Conclusion & Future Scope
7/7
CONCLUSION
Designed a combinational smart home security system.
Used basic OR and AND logic gates.
Implemented A = S(D + W + M).
Truth table and Logisim tests verify expected output.
Demonstrates a practical application of digital logic.
FUTURE SCOPE
Add multiple security zones.
Add password/keypad-based activation.
Add buzzer and visual indicators.
Connect the logic system to real sensors.
Explore IoT-based extensions as future work.
THANK YOU